## Slide 1: A Science Project: Swift Serial Chat
iOS Dev Scout (23 Nov 2016)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/SwiftSerial

## Slide 2: Modern networking options for apps
X
X
X
X

## Slide 3: Live Swift app Demo

## Slide 4: Swift for IoT @ iOS Conf 2016

## Slide 5: Swift Linux Serial Port library
https://github.com/yeokm1/SwiftLinuxSerial
Deprecated

## Slide 6: Updated Swift Serial Port library
https://github.com/yeokm1/SwiftSerial
Mac and Linux compatible
Swiftier: No more C in Swift!
Thanks to Jay Jun’s pull request
  https://github.com/yeokm1/SwiftLinuxSerial/pull/1

## Slide 7: Subh: Why not give a talk about your Swift Serial library?

## Slide 8: Agenda
What is a Serial Port?
My hardware setup
Walkthrough of original Swift Linux Serial
Learning points of Jay Jun’s pull request
My cross-platform command-line Swift chat app

## Slide 9: What is a Serial Port?
Hardware complying to RS-232 standard
Introduced in 1962 by Electronic Industries Alliance
Standardised as RS-232C in 1969
Vintage consumer usage
  Modems
  Mouse
  Point-to-point network
  Obsolete by 2000s
Modern Usage
  Medical Devices
  Scientific equipment
  Industrial Control Systems
  Uninterruptible Power Supply
  Simpler/Cheaper to implement and longer distance (300m) compared to USB
Male DE-9 connector
Traditional DB-25 connector

## Slide 10: RS232 Hardware Pinout
Pins | Name | Function
1 | Data Carrier Detect (DCD) | Device is connected
2 | Receive (RD) | Receive data
3 | Transmit (TD) | Transmit data
4 | Data Terminal Ready (DTR) | Ready to start a session
5 | Ground | Zero reference voltage for transmission
6 | Ringing Indicator (RI) | Phone is ringing!
7 | Clear to Send (CTS) | Hardware flow control (You can send data now!)
8 | Request to Send (RTS) | Hardware flow control (Can I send data to you?)
9 | Data Set Ready (DSR) | Ready to receive commands or data
http://www.db9-pinout.com/

## Slide 11: RS232 Communication Parameters
Baud Rate (Speed: bits/s)
  Linux max = 4 million bits/s
  Mac max = 230400 bits/s
Data bits
  Indicates frame size
Parity
  Error detection
  Even/Odd/None
  Makes number of 1 bits count even/odd
Stop bits
  Number of bits to indicates end of frame
Hardware flow control
  CTS/RTS Pins
Software flow control
  Xon/Xoff = Transmit on /Transmit off
https://learn.sparkfun.com/tutorials/serial-communication/rules-of-serial

## Slide 12: Hardware setup
Thinkpad T400 (2009)
Linux Mint 18
FTDI FT232 USB-Serial adapter
Macbook Pro Retina 15 (Late 2013)
macOS Sierra
Prolific PL-2303 USB-serial adapter
Null-modem cable

## Slide 13: Simple null modem cable
GND <-> GND
TX -> RX
RX <- TX
http://digital.ni.com/public.nsf/allkb/1EE0DD8AF67922FA86256F720071DECF

## Slide 14: Original Swift Linux Serial code
https://github.com/yeokm1/SwiftLinuxSerial/blob/master/Sources/SwiftLinuxSerial.swift
Enums for
  Baud rate
  Data bits
  Stop bits
Termios configuration structure
  c_cc C fixed array as Swift tuple
Reading and Writing bytes to port
  UnsafeMutable Pointers required for C functions

## Slide 15: Improved Swift Serial code by Jay Jun
https://github.com/yeokm1/SwiftSerial/blob/master/Sources/SwiftSerial.swift
Cross platform Mac and Linux
  Preprocessor directives:
    C directive is line level
    Swift directive is statement level
  Baud rates, port opening
Swiftier
  Guard statements
  typealias c_cc objects of termios struct, synonyms for pre-existing types

## Slide 16: My Swift chat app
Swift 3 command line desktop app
Uses Swift Serial library
Cross platform: Mac and Linux
Live chat between 2 machines
https://github.com/yeokm1/SwiftSerial/blob/master/Examples/SwiftSerialIM/Sources/main.swift

## Slide 17: Swift chat app interesting details
openPort()
  Using Swift Serial
prepareStdin()
  Don’t echo immediately to screen when user is typing
Background thread reads from port
  Mac: Grand Central Dispatch
  Linux: Posix threads (pthreads) as GCD (libdispatch) does not work with Swift Package Manager on Linux
  https://bugs.swift.org/browse/SR-397
Main thread reads from keyboard
  getchar() instead of readline() to read without pressing ”Enter”
  https://developer.apple.com/reference/swift/1641199-readline
Turn off output buffering
  setbuf(stdout, nil)
  If not multiple threads will have problems printing to screen
Print to screen without newline
  print(“string”, terminator:"")
  Default print prints the newline

## Slide 18: What is a “Science Project”?
By Raymond Chen
Principal Software Engineer, Microsoft
Joined 1992
Runs a blog “Old New Thing”
Mar 2013 post: https://blogs.msdn.microsoft.com/oldnewthing/20130319-00/?p=4913
Raymond Chen image from: http://www.dailytech.com/Microsoft+Exec+Reveals+Steve+Ballmer+Created+Original+Blue+Screen+of+Death+Message/article36512.htm

## Slide 19: A Science Project by Raymond Chen
A feature that is really cool and challenging from a technological standpoint but is overkill for the user-scenario:
  Networked bouncing ball screen saver for computers in a building
Requires hardware few people have:
  Tablet with 2 touch-enabled screens
Trying to solve a problem that nobody really considers to be a problem. You're doing it just for the Gee Whiz factor.
Taken from: https://blogs.msdn.microsoft.com/oldnewthing/20130319-00/?p=4913

## Slide 20: Any questions for a world without these?
X
X
X
X